## Slide 1: ENERGY VALVE 3.0 Solving Low Delta T Leveraging IoT

## Slide 2
Agenda
  Low Delta T
  Features and Benefits
  Success Stories
  Product Range Overview
  Industry Recognition
Notes: Agenda Slide
  A guide through the presentation starting with the problem that the Energy Valve solves Low Delta T
  Then moves to the solution in the Energy Valve describing an overview for those that are new to the energy valve and then to the features of EV3
  Overview of a couple of success stories more are available on Energy Valve.com
  Line overview showing wide flow and pressure range and pricing
  Industry recognition as a closing showing the success and acceptance of the product in the market

## Slide 3: Low Delta T Syndrome is Industry Wide
Notes: Low Delta T Syndrome is Industry Wide
  This slide shows helps set the stage for the problem there have been numerous studies and papers written explaining the impact of Low Delta T. A simple Google search for Low Delta T Syndrome reveals 1.2 million findings related to the topic

## Slide 4
Coils and valves are not sized properly
Systems are not dynamically balanced
Coils foul and degrade with age or lack proper maintenance
Too much water is delivered
Low Delta T May Occur When
Notes: Low Delta T may occur when
  Oversized Valves have low valve authority. This authority is exasperated during low load conditions.
  Systems are not dynamically balanced. Systems are typically balanced which is performed at design conditions which does not occur often typically only a handful of days a year. Systems change over time from maintenance or additions to system and Re-balancing is not common the Energy valve dynamically balances at all loads offering system stability and efficient operation
  Coils degrade over time. Without proper maintenance, the coil output is reduced leading to low heat transfer.
  Flow rate in excess of what it needed leads to Low Delta T overflowing the coil this point transitions to the next slide to explain coil behavior

## Slide 5: Low ΔT Reduces Heat Transfer at the Coil
Increased flow does not always produce more power instead it saturates the coil.
Notes: Low Delta T Reduces Heat Transfer at the Coil
  Basic explanation of the relationship between coil power and Delta T. Red scatter is data points of coil power with a yellow best fit line to normalize the data Blue scatter is data points of coil power with a blue best fit line to normalize the data
  As flow increases Delta T decreases
  In this example the coil curve starts to flatten and saturate at about 55 GPM and additional flow is being wasted as it is not producing additional BTU

## Slide 6
FLOW
DELTA T
$ PER TON/H RELATIVE TO DELTA T
LOW
MEDIUM
HIGH
LOW
MEDIUM
HIGH
42° F
Entering water
Return water
50° F
58° F
16°F
8°F
Central Plants Increase Rate for Low Delta T
Notes: Central Plants Increase Rate for Low Delta T
  Central Plants charge based on the Delta T the lower the Delta T the higher the rate
  Low Delta T forces the chiller plant to meet a volumetric increase
  They also have demand hours that in peak times the charges are even higher similar to how electric company peak hours
  It is not un common for charges for low Delta T to be in the order of $40,000 per month

## Slide 7
  Energy Valve 3.0
The world’s most advanced pressure- independent valve
Notes: Energy Valve 3.0
  Here is the introductory slide to the EV3.0
  A significant investment by Belimo in terms of engineering resources and capital one of the largest Belimo projects
  New Features will be in the following slides

## Slide 8: Energy Valve Overview
1
4
3
2
1
Actuator Webserver, data logger, BACnet, Modbus, MP-Bus, Cloud capability
2
Electronic Flow Meter True Flow, Wet calibrated
3
Temperature Sensors
Platinum based RTD for supply and return, allowing BTU measurement
4
Logic Delta T Management, Cloud Optimization, Power Control algorithm
Measure, Observe, Record and Trend Performance Data

## Slide 9
  New Features
Cloud-Based
Services
Enhanced User
Interface
Enhanced Delta T Management
Glycol Monitoring
Ultra Sonic Flowmeter

## Slide 10
Enhanced Delta T Management

## Slide 11: More Savings
Coil Optimization
Expanded Delta T range 2°F to 100°F [1.1°C to 55.5°C]
Dynamic coil performance provides transparency of changes in load and usage patterns
Integrated Delta T setpoint
Notes: More Savings
  Expanded Delta T Range for heating applications, Heat exchangers and helps us position to achieve EN1434 European heat metering standard. 2 Degree Delta T is not common in systems but can be utilized to analyze a system if desired.
  Transparency of load updated dynamically providing visibility to load and usage patterns, and predictive coil maintenance.
  The Delta T set point suggestion is integrated and exporting to the data analysis tool is no longer needed
  The lower limit on the Delta T Manager has been enhanced providing more savings at partial load. This is an option which is selected in webview. The default is still 30% of Vmax, the new option can go all the way down to 10% of Vnom

## Slide 12
Ultrasonic Flow Meter

## Slide 13: Advanced Ultrasonic Sensor Technology
1
4
3
2
1
True Flow Actual flow measurement as opposed to calculation like mechanical PI valve
2
Wet Calibrated Individually calibrated to ensure accuracy and repeatability
3
Temperature and Glycol Compensation
Ensures accuracy over entire temperature range and varying glycol concentration
4
Glycol Monitoring
Provides actual glycol % for safe operation and optimized heat exchange
Notes: Ultrasonic Flow Meter
  Belimo Designed Ultrasonic launching in September
  Rangeability 100:1
  6 X higher resolution than Electromagnetic
+/- 2% reading of flow rate
How glycol Monitoring works is by using the internal temperature sensor in the ultrasonic flow meter and the speed of sound from the flow meter. Having these two pieces of information there is a cross reference table in the actuator of speed of sound and temperature that indicates for specific speeds of sound and temperatures it solves for the glycol %.

## Slide 14
Glycol Monitoring

## Slide 15: Glycol Monitoring Ensures concentrations meets design needs
Glycol content below the design concentration:
System at risk of freezing
Imposing costly repairs
Risk of damaging the building
Glycol content at ideal level:
Increases overall heat transfer
Increases pumping efficiency
Reduces operating costs
Glycol content above the design concentration:
Increases fluid viscosity which reduces pumping efficiency
Heat transfer effectiveness of the coil degrades
Critical zones may be starved
Results in loss of comfort
Notes: Glycol Monitoring Benefits
  Glycol concentration and pump efficiency are linked the higher the concentration the more viscous or thick the media becomes creating additional pressure requiring additional pump head
  Glycol concentration and heat exchange are linked and excessive concentrations have a negative effect on heat exchange and will create inability to hit discharge air set point
  In cold environments glycol concentration is essential not having this could cause coils to freeze and or become damages causing costly repairs to the building and system
  There is also a financial savings having this monitoring integrated into the valve. One eliminates the need for additional refractometer, eliminates the need for additional control point to integrate this refractometer ($600-$1500) also glycol is not wasted being added in excess as it is now continuously monitored

## Slide 16
Enhanced User Interface

## Slide 17: Enhanced User Interface
Streamlined design Live data points
Notes:   The User Interface has been completed redesigned with a streamlined approach. This Overview page is the main page for information and data points on the screen are live showing data in real time and upon clicking on them a chart of historical operation can be viewed. Also if there is an error on a data point such as flow or temperature. There are help Icons that take the user directly to the trouble code where there will be suggestions on how to correct the error

## Slide 18: Enhanced User Interface
Guides through valve set up
Notes:   Startup wizard provides immediate familiarity with the valve guiding the user through set up. Runs when the valve is initially powered up and settings selected during ordering are already populated Can be run as often as desired it is located on the application page of the setting menu

## Slide 19: Enhanced User Interface
Software update capability
Notes:   It is possible to have software updates via the cloud if connected or can be loaded on the actuator if not connected to the cloud. These will be for updated related to security, and operation not upgrading from EV2 to EV3

## Slide 20: Enhanced User Interface
Customize job specific information
Notes:   Customizable pages provide ability to define AHU location and other user specified information Also during the startup assistant there is possibility to add site information The first two entries on the left will be displayed on the webpage and the others will display when the actuator is connected to the cloud.

## Slide 21
Enhanced User Interface
KPI’s & multiple data file downloads
Notes: Key performance indicators including, time in particular control mode, Delta T Manager activity, total flow, energy and operational statistics graphically illustrated

## Slide 22
Enhanced User Interface
Improved
troubleshooting
information
Notes:   Improved troubleshooting with informational help buttons that provide suggestions to correct errors

## Slide 23: Enhanced User Interface
Commissioning
report provides
verification of setup
Notes: Generates a PDF of the valve settings that can be used to verify valve set up and prove correct set up

## Slide 24: Enhanced User Interface
Save and reload settings from
one valve to another
Notes: Allows for setting up multiple valves quickly exports an XML file that can be loaded into another valve. The valves need to be the same size but the file can be edited to adapt to different size valves

## Slide 25: Enhanced User Interface
User
administration
Notes:   User Administration allows for addition and deletion of users and full password functionality. This is for advanced users that require the ability to change passwords. There is also a recommendation to change the password at the end of the startup assistant

## Slide 26: Enhanced Communication Unlike any actuator on the market
2-10 VDC
0.5 -10 VDC
ANALOG
Notes:   No other actuator on the market today has more ways to communicate
  New for 3.0 Modbus and cloud connectivity

## Slide 27
Cloud-Based
Services

## Slide 28: Leveraging the Belimo Cloud
Cloud-Based Services
Remote cloud communication to monitor energy usage and leverage system data
Advanced Efficiency
Increase plant efficiency and mitigate the Low Delta T syndrome to reduce pumping and chiller/boiler operating costs
Automatic Optimization
Capture system data to automatically improve coil and system performance via advanced analytic technology
Notes:   Bellimo has always been a technology leader so the transition to cloud technology is a natural step.
  The competitive edge will be leveraging the data, it is all about the data
  With Belimo having valves located all over the world and having the same valve characteristics in terms of flow curves and geometry the missing variable is the system data. Having this system data allows Belimo to further advance the products in terms of optimizing systems. Machine learning can crunch this data to drive valve and system performance
  Belimo is taking efficiency to a higher level

## Slide 29: Energy Valve 3.0 Cloud Services Advanced optimization with multiple benefits
LIFETIME
DATA ACCESS
PERFORMANCE REPORT
INCREASE WARRANTY TO 7 YEARS
OPTIMIZATION OF DELTA T AND FLOW SETTINGS
SOFTWARE
UPDATES
ONLINE SUPPORT
Notes:   The cloud based services are a complement to the product and are offered at no additional cost and will be discussed in detail in the upcoming slides
  Now Optimization is automatic via the cloud the optimal Delta T and flow set points and be sent to the valve automatically or can be set manually by the user. Either way they receive an email of the proposal/changes
This now provides an advanced level of optimization with cloud based data optimization via machine learning. It takes the labor out of analyzing data.

## Slide 30
OPTIMIZATION OF DELTA T AND FLOW SETTINGS
Better performance and system stability
Ensures effective use of the Delta T Manager
Cost savings through efficient operation
Notifications of any system changes
Notes:   This ensures that the Delta T Manger is being used and being used correctly and effectively.
  Operating at the optimal settings will provide better performance and overall system stability.
  Utilizing the Delta T Manager optimally will also provide pump savings operating the coil at the design Delta T
  The customer will receive via email recommendation for Delta T and flow set points based on the data from that valve. There needs to be at least two months of data loaded for a recommendation
  These can be either manually loaded or automatically loaded. If the valve is used for both heating and cooling which is determined by the customer and needs to be entered when requesting optimization of Delta t and flow settings it can only be implemented manually.

## Slide 31
PERFORMANCE REPORTING
Automatically generated performance report with key insights
Eliminates need to analyze data
Allow for predictive maintenance of coil performance and easy ROI analysis
Notes: Performance reporting
  Quarterly report of valve operation including total flow rates, Energy usage, Delta T Manger usage, trouble codes triggered and coil plot
  This proves valve performance and operation
Provides a tool for predictive maintenance from transparency of coil performance

## Slide 32
BELIMO ONLINE SUPPORT
Real time troubleshooting reduces downtime
Fast response
Direct connection to Belimo experts
Notes:   Allows for our technical support team to log directly into the valve seeing real time of set points.
  Will reduce down time from faster response

## Slide 33
SOFTWARE UPDATES
Latest software and security updates automatically provided for maximum productivity and reliability
Uninterrupted service
Direct notification via email
Notes:   Updates for security and productivity only
  This will not be used to upgrade from EV2 to EV3.0
  Can be automatically loaded or user loaded either way will receive an email that they are available

## Slide 34
LIFETIME DATA ACCESS
Secure data and password management
Lifetime access for future optimization
Easy-to-use interface
Single, secure repository
Simplified overview of KPIs
Notes: Lifetime data access
  Provides value in terms of data storage eliminating the user from purchasing additional storage
  Consolidates all data for all valves in one location, very helpful if the user has multiple buildings
  Stored, backed up and secure for the lifetime of the valve
Data export is similar to the .csv format from the actuator

## Slide 35
EXTENDED WARRANTY
Peace of mind
Reduce maintenance budget
Reminder of warranty status
Statement of Belimo quality

## Slide 36
One Valve So Many Benefits
Cloud-Based
Services
New User
Interface
Enhanced Delta T Management
Glycol Monitoring
Ultra Sonic Flowmeter
Hydronic Balancing
Pressure Independent Control
Notes: Seven Functions in one valve

## Slide 37: Most Capable Valve in the HVAC Industry
Feature | Typical PI* | Original Energy Valve | Energy Valve 3.0
IoT Device |  |  | 
Cloud Analytics |  |  | 
Glycol Monitoring |  |  | 
Commissioning Report |  |  | 
True Flow |  |  | 
Dynamic Balancing |  |  | 
Energy Meter |  |  | 
Power Control |  |  | 
Delta T Manager |  |  | 
Live Data |  |  | 
Coil History |  |  | 
CCV Technology** |  |  | 
Leakage | ANSI Class IV | 0% | 0%
High Close-off |  |  | 
Low Minimum Pressure Drop |  |  | 
Field Configuration |  |  | 
Bus Communication |  | BACnet MS/TP or IP and MP Bus | BACnet MS/TP or IP, Modbus RTU or TCP/IP and MP Bus
Password Configuration |  |  | 
Set-Up Wizard |  |  | 
5-Year Warranty |  |  | 
7-Year Warranty with Cloud Access |  |  | 

## Slide 38
CASE STUDY
Massachusetts Institute of Technology (MIT)
Average Delta T rose from 6.15°F to 12.14°F, reducing chilled water flow by
Annual savings were estimated to be as high as
$1.5 million
49%
Success Story
Massachusetts Institute of Technology (MIT)
Average Delta T rose from 6.15°F to 12.14°F, reducing chilled water flow by
49%
Annual savings were estimated to be as high as
$1.5 million
Notes: MIT Success story
  One of our most prestigious success stories
  Building and Project Details
    150,000 sq. ft. on 3 floors
    Built in 1947 (originally had its own dedicated chiller, later converted to campus district cooling)
    6 AHU provide majority of the cooling
    Average delta T coil = 6.15°F before Delta T Management
  Results
    Aug 9 - Oct 9, 2010 DT = 6.15 F
    Aug 9 - Oct 9, 2011 DT = 12.14 F

## Slide 39
Success Story
Hillsdale College Mossey Library & Delp Hall
Delta T Increased 3-7°F to 10-12°F reducing usage of chiller by
  300 hours/year
Electricity consumption reduced by as much as
16%
Notes:   In the spring of 2013, Hillsdale College made the decision to install three Energy Valves as part of a pilot test. Two of the valves were installed in the campuses
60,800 SF Mossey Library and the third in Delp Hall, a 20,000 SF square foot
  Increased chilled water Delta T across coils to their design of 10 -12°F
  Used feedback data from Energy Valve to control pumps with variable frequency drives (VFDs), allowing for more precise control of the chilled water
loop without sacrificing the AHUs call for cooling during occupied times.
  After the success of the pilot test, the decision was made to install additional Energy Valves throughout the campus. Over the course of the next year (from May of 2014 to May of 2015), 24 Energy Valves were installed in 11 buildings across the main chilled water loop (sizes from 1/2 to 4-inch). In some coils, deltaT’s were seen as high as 30°F while sufficiently maintaining the air handler’s desired discharge air cooling temperature.

## Slide 40: Wide Range of Flow and Pressures
Size: ½” to 2”
GPM: 1.65 to 100
Ends: NPT
Size: 2.5” to 6”
GPM: 38 to 713
Flange: ANSI 250
Size: 2.5” to 6”
GPM: 38 to 713
Flange: ANSI 125
New Ultrasonic
Q3 Launch

## Slide 41: Pricing NPT
ACTUATOR PART # |  |  |  |  | LRX 24-EV | LRX24-EV-G | NRX24-EV | NRX24-EV-G | ARX24-EV | ARX24-EV-G | AKRX24-EV | AKRX24-EV-G
GLYCOL MEASUREMENT |  |  |  |  |  | · |  | · |  | · |  | ·
MODEL # | GPM | SIZE | BODY PRESSURE RATING (PSI) | CLOSE-OFF PRESSURE (PSI) |  |  |  |  |  |  |  | 
EV050S-055 | 5.5 | 0.5” (15) | 360 | 200 | $1,341 | $1,740 |  |  |  |  | $1,949 | $2,348
EV075S-103 | 10.3 | 0.75” (20) |  |  | $1,385 | $1,784 |  |  |  |  | $2,037 | $2,436
EV100S-182 | 18.2 | 1” (25) |  |  | $1,473 | $1,872 |  |  |  |  | $2,280 | $2,679
EV125S-285 | 28.5 | 1.25” (32) |  |  |  |  | $1,947 | $2,346 |  |  | $2,354 | $2,753
EV150S-396 | 39.6 | 1.5” (40) |  |  |  |  | $2,090 | $2,489 |  |  | $2,572 | $2,971
EV200S-761 | 76.1 | 2” (50) |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  | $2,472 | $2,871 | $2,887 | $3,286
EV200S-1000 | 100 | 2” (50) |  |  |  |  |  |  | $2,472 | $2,871 | $2,887 | $3,286
7 Models (-G Glycol models)
Sizes: ½” to 2”
Flow Range: 5.5 GPM to 100 GPM

## Slide 42: Pricing ANSI 125
ACTUATOR PART # |  |  |  |  | ARX24-EV | GRX24-EV | AKRX24-EV | GKRX24-EV
MODEL # | GPM | SIZE | BODY PRESSURE RATING (PSI) | CLOSE-OFF PRESSURE (PSI) |  |  |  | 
EV250S-127 | 127 | 2.5” (65) | ANSI 125, STANDARD CLASS B | 100 | $8,451 |  | $9,760 | 
EV300S-180 | 180 | 3” (80) |  |  | $10,968 |  | $12,278 | 
EV400S-317 | 317 | 4” (100) |  |  |  | $12,727 |  | $14,350
EV500S-495 | 495 | 5” (125) |  |  |  | $15,749 |  | $17,372
EV600S-713 | 713 | 6” (150) |  |  |  | $20,132 |  | $21,756
5 Models
Sizes: 2½” to 6”
Flow Range: 127 GPM to 100 GPM

## Slide 43: Pricing ANSI 250
ACTUATOR PART # |  |  |  |  | EVX24-EV-L | EVX24-EV-B | AVKX24-EV-L | AVKX24-EV-B
MODEL # | GPM | SIZE | BODY PRESSURE RATING (PSI) | CLOSE-OFF PRESSURE (PSI) |  |  |  | 
EV250S-127-250 | 127 | 2.5” (65) | ANSI 250, Standard Class B | 310 | $12,210 |  | $13,755 | 
EV300S-180-250 | 180 | 3” (80) |  |  | $14,735 |  | $16,280 | 
EV400S-317-250 | 317 | 4” (100) |  |  |  | $16,964 |  | $18,509
EV500S-495-250 | 495 | 5” (125) |  | 296 |  | $21,335 |  | 
EV500S-495-250 | 495 | 5” (125) |  | 202 |  |  |  | $22,880
EV600S-713-250 | 713 | 6” (150) |  | 215 |  | $25,133 |  | 
EV600S-713-250 | 713 | 6” (150) |  | 135 |  |  |  | $26,678
7 Models
Sizes: 2½” to 6”
Flow Range: 127 GPM to 100 GPM

## Slide 44: Industry Recognition
ControlTrends 2014
Energy Saving Product of theYear
ControlTrends 2012
Best commercial product of the year
2015 Energy Show
Best Energy Efficient Product
Acrex 2015
Winner of award of excellence
BCIA Awards 2013
Technical Innovation of the Year
2013 Building Efficiency Award
Best energy efficient automation product
HVR Awards 2012
Air-conditioning product of the year
Silver Trophy
Silver Trophy Award 2013
Winner of Energy Smart Automation Award
Shanghai Energy IAC 2014
Golden Key Award
ACME 2016
Winner of Innovation Award
2017 AHR Innovation Award
Finalist in the Category of Building Automation
2014 AHR Innovation Award
Winner in the Category of Building Automation

## Slide 45: For more information and access to useful tools and resources, visit energyvalve.com
FIND US
BELIMO Americas
33 Turner Road Danbury, CT 06810
CONTACT
Phone: +1-800-543-9038
Fax: +1-800-228-8283
E-mail: marketing@us.belimo.com
WEBSITE
www.belimo.us